Title: 16 pt bold; left justify

Influence of sorption heterogeneity on the transport of nonlinearly sorbing solutes

(Skip 2 lines)

Author name: 12 pt bold caps; left justify; superscript to indicate address

Ute Döring1, Uwe Jaekel2 & Harry Vereecken2

Address 1. 9 pt,  italic except no. 1, left justify

1  Geology Department, Martin-Luther University, Domstrasse 5, D-06108 Halle (Saale), Germany

(Skip 1 line)

E-mail address of corresponding author: 9 pt; all lower case

doering@geographie.uni-halle.de

Address 2. 9 pt,  italic except no. 2, left justify

2  Jülich Research Centre, D-52428 Jülich, Germany

(Skip 1 line)

Abstract: 11 pt; fully justify; word “Abstract” in bold

Abstract The effect of spatially variable aquifer parameters such as sorption capacity and hydraulic conductivity on reactive solute transport was investigated by stochastic numerical simulations. Heterogeneity of the sorption capacity was about half as large as heterogeneity of the hydraulic conductivity. Variable Freundlich sorption parameters had less influence on the expected plume velocity than on the spatial distribution (second order moment) of the dissolved and sorbed mass. A comparison between simulated and real tracer plumes revealed significant discrepancies concerning the dissolved concentrations. Due to their order of magnitude these discrepancies cannot be attributed to physico-chemical sediment heterogeneity.

Key words: 9 pt; fully justify; can make 2 lines;

“Keywords” in bold

Keywords aquifer; numerical simulation; stochastic; uranin; tracer test; sediment properties

(Skip 2 lines)

Level 1 heading: 12 pt bold caps; left justify; skip 2 lines before 1 line after heading

Introduction

(Skip 1 line)

Do not indent 1st paragraph after level 1 and level 2 headings; indent subsequent paragraphs 0.7 cm

Put variables in both equations and text in italic

In an integrated approach of field experiments, laboratory experiments and numerical simulations both physical and physico-chemical aquifer heterogeneities were investigated. About 400 sediment samples were analysed and statistically evaluated with respect to the following characteristics: grain size distribution, calculated hydraulic conductivity, K, cation exchange capacity, CEC, and the specific surface area. On 70 samples the vertical variation of the Freundlich sorption parameters k and n was determined for uranin (C20H10O5Na2) sorption on the aquifer sediments (Döring, 1997). The impact of the measured sorption heterogeneity was investigated by stochastic numerical simulations which were then compared to the observed uranin transport at the test site.

(Skip 2 lines)

Level 1 heading

Results

(Skip 1 line)

Level 2 heading immediately after level 1 heading: 12 pt bold lowercase with initial capitals for first word and proper nouns; left justify; skip 1 line after heading

Sediment heterogeneity

(Skip 1 line)

The following results refer to measurements of the 3 m aquifer interval which was most relevant during the tracer tests. Table 1 shows that the vertical spatial variation of K was usually twice as large as the variation of physico-chemical sediment properties. A similar ratio was found in the horizontal direction but with higher variances (Döring, 1997). According to other test sites, the order of heterogeneity was compared by determining the mean variation which is defined as the ratio of values corresponding to one standard deviation above and below the mean. The vertical correlation lengths of a few decimetres compare very well for all parameters, they are also in the range of values reported for other Quaternary test sites. Since K and the physico-chemical parameters show a weak negative correlation (correlation coefficient c. –0.7), physico-chemical heterogeneity should lead principally to an enhanced spreading of the reactive solutes.

(Skip 2 lines)

Table heading: 10 pt; fully justify; full width; put “Table 1” in bold

(Skip 1 line)

Leave 0.75 cm between table and text

Tables: 10 pt; 14.8 cm wide; 9 pt or 8 pt  type size may be used for body of table if this is necessary to make table fit across page;

units in parentheses;

left justify but decimally align numbers when appropriate ;

½ pt rules above and below column headings and below bottom row of table;

Note: no internal rules

Table 1 Spatial variation of hydraulic conductivity (K), physico-chemical sediment parameters and uranin sorption capacity (S) in the vertical direction.

|  | N | Mean | –1 STD | +1 STD | Mean variation | (v (m) (exponential) |
| --- | --- | --- | --- | --- | --- | --- |
| K (m s-1) | 120 | 8.0 × 10-4 | 3.8 × 10-4 | 1.7 × 10-3 | 4.5 | 0.4 |
| CEC (meq kg-1) | 50 | 5.5 | 4.0 | 7.6 | 1.9 | 0.4 |
| Clay (M%) | 50 | 2.3 | 1.8 | 3.0 | 1.7 | <0.2 |
| Fines (M%) | 50 | 8.8 | 7.1 | 10.8 | 1.5 | 0.6 |
| Surface (m² g-1) | 50 | 0.94 | 0.46 | 1.88 | 4.1 | trend |
| S, k var. (µg kg-1) | 16 | 22.9 | 15.4 | 30.4 | 2.0 | not det. |
| S, n var. | 16 | 22.9 | 20.9 | 26.3 | 1.3 | not det. |
| S, k+n var. | 16 | 22.9 | 14.8 | 31.1 | 2.1 | not det. |

(v = vertical correlation length, exponential model.

STD = standard deviation.

Fines = fraction < 0.2 mm.

S, k+n var. = sorption capacity considering variable k + n parameters.

S, k var. = sorption capacity considering variable k parameter only.

S, n var. = sorption capacity considering variable n parameter only

Level 2 heading: 12 pt bold lowercase with initial capitals for first word and proper nouns; left justify; skip 2 lines before and 1 line after heading

Stochastic simulations

(Skip 1 line)

Note layout of units—negative powers used not “/”

Numerical modelling was used as a tool to investigate the effect of heterogeneities in K and sorption parameters on solute transport. The consideration of heterogeneity required stochastic flow models and transport models which were developed for massively parallel computers. A two-dimensional stochastic flow field was computed based on a K field with a mean value of 2 × 10-3 m s-1, a variance of ln(K) of 0.81 and an isotropic horizontal correlation length of 5 m. The resulting velocity field had a mean value of 1.7 m day-1 with a range between 0.2 and 9.1 m day-1. Solute transport was calculated with a particle tracking code developed by Neuendorf (1997), each simulation considered 10 × 106 particles. While keeping the velocity field constant, solute transport was simulated for 30 realizations with stochastically generated sorption fields. None of the variables (K, n, k) were assumed to be correlated. A simulation with homogeneous sorption was also performed for comparison. In Table 2 the input data are listed: all sorption parameters were measured on the 3 m aquifer interval described in the previous section.

(Skip 1 line)

Table 2 Sorption input parameters for numerical simulations.

|  | Mass (µg) | k | n | vark | varn | (h (m) |
| --- | --- | --- | --- | --- | --- | --- |
| Hom. sorption | 1.1 × 108 | 0.55 | 0.81 | - | - | - |
| Het. sorption | 1.1 × 108 | 0.55 | 0.81 | 0.027 | 0.001 | 5 |

(h = isotropic horizontal correlation length, exponential model.

Var = variance; Hom. = homogeneous; Het. = heterogeneous.

(Skip 1 line)

The effect of spatially variable k and n values on the expected plume velocity <v1> is demonstrated in Fig. 1(a). The homogeneous case is also shown. The variability of the expected plume velocity is quite small as indicated by the narrow curves representing the range of one upper and one lower standard deviation (STD). The coefficient of variation (CV) ranges between 13% for the first 40 days and less than 2% after 140 days. Therefore the impact of heterogeneity of nonlinear sorption on the plume displacement decreases with time. The nonlinearity of the sorption behaviour seems to be more important for the long-term transport velocity than the impact of spatially variable sorption parameters. Similar results were described by Bosma et al. (1996).

Fig. 1 Evolution of (a) average longitudinal plume velocity <v1>, and (b) longitudinal second-order moment <S11> for heterogeneous and homogeneous sorption.

Figure: indent 2.54 cm if less than 12.2 cm wide

Place figures between 12.2 and 14.8 cm wide at left-hand margin

Centre figures between and 14.8 and 17 cm wide

Check all figures are legible. The labelling must not be too small to read!

Figure caption: 10 pt; fully justify; indent 2.54 cm; put “Fig. 1” in bold

Leave 0.75 cm between caption and text

Label parts of a figure (a), (b), (c) etc.

The effect of spatially varying sorption parameters on the expected second order spatial moment <S11> of the solute plume is shown in Fig. 1(b). Again, the case with homogeneous sorption is included. As for the transport velocity, the expected second order moments of the heterogeneous case agree very well with the moments calculated for constant sorption coefficients. The CV however is considerably larger, ranging roughly between 50% and 20%. The highest values occur at the initial phase. Heterogeneous sorption therefore affects the shape of the plume more than the mean displacement time. For the sorbed mass, the CV was almost 100% at the beginning, but also decreased to about 20% at the end of the simulation.

Modelling vs reality

Although sorption heterogeneity could be considered in these investigations, there was still a large discrepancy between simulations and the real plume transport. Most significant for the tracer tests was a constant mass loss of uranin (but also of lithium and bromide) which in its order of magnitude can neither be attributed to physical nor to sorption heterogeneity. From field and laboratory observations we rather think that chemical reaction processes such as nonequilibrium sorption or some degree of non-reversibility are the dominating solute transport processes.

Do not leave 1 and 2 level headings at bottom of page without any text below; start heading and text on next page

References

References: 8½ pt; 0.7 cm hanging indent; entries listed alphabetically;

Journal titles and book titles in italic;

volume numbers of journals in bold;

titles in another language are followed by English translation in parentheses.

Note there is a space between initials

Bosma W. J. P., Van der Zee, S. E. A. T. M., Van Duijn, C. J. (1996) Plume development of a nonlinearly sorbing solute in heterogeneous porous formations. Wat. Resour. Res. 32(6), 1569–1584.

Döring, U. (1997) Transport der reaktiven Stoffe Eosin, Uranin und Lithium in einem heterogenen Grundwasserleiter (Transport of reactive substances eosine, uranin and lithium in a heterogeneous aquifer). PhD Thesis. Report no. 3354, Research Centre Jülich.

Neuendorf, O. (1997) Numerische 3D-Simulation des Stofftransportes in einem heterogenen Aquifer (Numerical 3D solute transport simulation in a heterogeneous aquifer). PhD Thesis. Report no. 3421, Research Centre Jülich.

Please use English British spelling; e.g.

- use groundwater (instead of ground water or ground-water)

- use modelling and modeller (instead of modeling and modeler)

- use colour, vapour, favour (instead of colour, vapor and favor)

Insert figures and Tables soon after they are mentioned in the text

# Text boxes

Insert or cut and paste graphics for figures.